## Slide 1: Discussion Regarding Feature to be Used for Disaggregation
Manoj Gulati
20-11-2014

## Slide 2: Possible features that can be explored for disaggregation.
Common Mode/ Differential Mode component of EMI ( Our Current Focus)
Differential Mode of EMI with Lower cut-off freq. (9 kHz earlier it was 60 kHz in our design)
Harmonic analysis (up to 50th harmonic i.e. 2.5 kHz)

## Slide 3: Few Challenges with Common mode separation
To remove common mode component of EMI, nowadays many appliances don’t have Earth pin in power cord.
  Earth function is provided either using metal body of appliance or by adding a transformer and then shorting earth pin of appliance to neutral on secondary side.
  It can’t be directly shorted to neutral as user may connect the power cord in a reverse fashion and neutral will become hot which can be risky.
Note: In such appliances DM component will be significant as that’s the only path.

## Slide 4: Harmonic Analysis
Open datasets are available (Plaid CMU, REDD MIT), but so far no paper exist using frequency domain harmonic analysis for disaggregation.
More information is present in harmonics as we have 50 relative amplitudes which will show distinct behaviour with different appliances.
It can be used for fault detection at building level. (Leeb’s group at MIT tried this at appliance level)

## Slide 5: Differential EMI Sensing (with lower cutoff)
Earlier this was not possible as we were using signal analyser for measuring frequency spectrum but now we can do this as we are capturing time domain data using MDO or Redpitaya and computing FFT locally.
This could give improved results.

## Slide 6: Major point to discuss
Whether to move on with Common mode and differential mode of EMI or start with Harmonics.
  I feel it’s good to explore both for one week rigorously and then decide based on experimental results. DOD: 5th December, 2014

## Slide 7: Help Required
Someone from industry/ Academics who has strong background in EMI testing , to benchmark our filters. (I can design new filter in one day but need to verify response as per EMI standards in comparison with LISN).
This company (CFL mfg.) is having EMI facility in Delhi but I don’t know anyone there.
NTL Electronics
Customer Name : Ms. Maya Kurian(Purchase)
Contact No. : 9899708390
e.mail : maya.kurian@ntlelectronics.com

## Slide 8: Updates
I am now maintaining a list of papers I have read on Git along with their brief overview after RM course.
Started with new filters for sensing phase and neutral voltage for separating CM and DM mode of EMI.
Tested only one appliance but need to scale up now to ensure results.