## Slide 1: Design of single-sided HPF to measure Vphase and Vneutral
7th October, 2014
Manoj Gulati

## Slide 2: Connection Diagram
Mains
Power Supply
Appliance Under Test
Phase
Earth
Neutral
R
R
C
R
R
R
C
R
0.1uF
0.1uF
100
100
70
70
70
70
Vneutral
Vphase
Node A
Node B
Node A
Node B
Vrms = 230V
50 Hz
Vp = 326V
Vrms = 230V
50 Hz
Vp = 326V
To MDO CH-2
To MDO CH-1

## Slide 3: Filter Parameters (Calculated and Measured)
Single-ended
Balanced Pi structure (to match input and output R value to 50 ohm)
(Calculated and Measured)
Output Impedance = 50 Ohm (Calculated and Measured)
Equivalent R = 50 Ohms
C = 0.1uF
Fc = 31.84 kHz (Calculated)
V(Node A) = 0.7149V (Calculated)
V(Node B) = 0.2944V (Calculated)

## Slide 4: Simulation Results

## Slide 5: Circuit Prototype

## Slide 6: Sensing System: Tektronix MDO 4104-06
4 Analog Input Channels
1 spectrum analyzer channel (50 kHz to 3 GHz)
In-built features like FFT Spectrum analysis and Spectrogram.
1 GHz Bandwidth
Up to 2.5GSa/s sampling rate
No. of points: 20000 max (Time domain)
Active Probing (Optional Adapter TPA-N-VPI)
  12dB Gain from (9kHz-6GHz) also meant for EMI measurements
Data export: USB storage similar to signal analyzer.

## Slide 7: Task for next week (14-10-2014)
Make two such circuits on a good quality PCB board.
Get Vphase and Vneutral data with a single appliance from MDO.
Compute Vcm and Vdm using Vphase and Vneutral data in MATLAB and compute FFT for this.
Match Vdm results with previous results from EMI paper.